## Slide 1: Auxiliary Power Consumption
Auxiliary power accounts for the power consumed by plant equipment and its auxiliaries.
Out of the total power generated by a Thermal Power Plant, nearly 8 to 10% of it is consumed by the plant equipment and machinery required to keep the plant operational.
Major equipments consuming auxiliary power :
Boiler feed pump
ID fans
PA fans
SA fans
Pulverizers
Electrostatics precipitators,etc

## Slide 2: Effect on power consumption due to changes in plant conditions
Auxiliary power consumption doesn’t just contribute to overall efficiency parameters, but an overtime change measured as % of total power generated can indicate degrading machine cycles or faults in the pipeline due to increasing age of the equipment.
Air leakage into boiler gas enclosure.
Degraded Boiler heating Surface –higher dry gas loss would increase power consumption
Higher draft loss due to air ingress and ash deposition.
Deterioration of generator stator windings due to increased stress and age
Deterioration of Turbine Steam Path Condition.

## Slide 3
Condenser pressure/ condenser cleanliness- air ingress and extent of tube pluggage. Contamination of feed water can cause changes in heat capacity, that indirectly affects boiler efficiency
Steam and water leaks from drains and vents.

## Slide 4: Plant Load factor
The auxiliary power is greatly influenced by the plant load factor. Many of the Indian power stations are operating at sub-optimal plant load factor that cause higher auxiliary power and decreased efficiency and performance.
Plant Load Factor (PLF) can be used as a measure to quantify the auxiliary power consumption.
Instantaneous plant load factor is given by :
Whereas the auxiliary power consumption of individual equipment is given by :

## Slide 5
Since auxiliary power of equipments have a baseline which is the set design value, it is actually the deviation which acts as a control parameter to optimize the the auxiliary power consumption. The formula for the deviation in AP of individual equipment is given by :
Measures to improve plant load factor include:
Quality of coal used - higher calorific value and low ash content coal reduces the flue gas flow, which decreases stress on ID fans.
Boiler efficiency - increased boiler efficiency reduces stress on BFP, PA fans and SA fans.
Turbine efficiency - increasing turbine efficiency ensures reduced stress on CWF pumps and alternator windings.

## Slide 6: Reducing auxiliary power consumption
Consider Variable frequency drives for Boiler feed pumps, fans and other major Auxiliaries.
Choose optimum margins on head and flow for Boiler feed pumps and fans, to attain best efficiency under actual operating conditions.
Design Boiler with best possible thermal efficiency
Leak proof duct design to avoid air ingress in order to reduce load on induced draft fan.
Ensure complete combustion in furnace, so that required steam generation can be achieved with optimum fuel quantity.
Minimise system drop (flue gas side , steam and water side) without affecting the Boiler performance

## Slide 7: Project overview
Based on the study of Thermal Power plants, Advanced Process Control (APC) and Auxiliary Power Consumption, following observations and conclusions of the Vikram Cement Works Power Plant have been made :
No control loop exists for coordinating boiler and turbine operations. An APC on top of existing control loops can help improve performance and efficiency
There is no continuous performance monitoring of the plant. A performance monitoring and reporting system can help in fine tuning of machinery and equipment during operation.
Installation of Variable Frequency Drive can reduce Auxiliary Power Consumption of various motors and pumps used in the plant.
Advanced controller for furnace pressure control can help in reducing auxiliary power consumption of PA and SA fans.

## Slide 8
5. Advanced Controller for fuel feed can improve and provide stable response to air and fuel feed. This model can tune fuel feed parameters so that the combustion cycle adjusts to any changes in fuel type/composition.