## Slide 1: Power Plant Cycles
A thermodynamic cycle is a series of operations, involving a heat source, a heat receiver, a machine and working substance.
Types of Power Plant Cycles:
Vapour Power Cycles
  Rankine Cycle
  Reheat Cycle
  Regenerative cycle
  Binary Vapour Cycle
Gas Power Cycles
  Otto Cycle
  Diesel Cycle
  Dual Combustion Cycle
  Gas Turbine Cycle

## Slide 2: Rankine Cycle
Rankine cycle is the theoretical vapor-liquid cycle on which steam power plant works. In a vapor cycle if the working fluid in a vapor cycle passes through various components of the power plant without irreversibility and frictional pressure drop, then the cycle is called as Ideal Rankine Cycle.

## Slide 3
The Efficiency of Rankine Cycle can be increased by the following methods:
Lowering the condenser Pressure
Superheating the steam to high temperatures
Increasing the Boiler Pressure
Rankine Cycle is modified into two types of cycles:
Reheat Cycle
  The purpose of a reheating cycle is to remove the moisture carried by the steam at the final stages of the expansion process.
Regenerative Cycle
  After emerging from the condenser (possibly as a subcooled liquid) the working fluid is heated by steam tapped from the hot portion of the cycle.